## Slide 1
Chapter 2 Configuration Space
Chapter 3 Rigid-Body Motions
3.2 Rotations and Angular Velocities
Chapter 4 Forward Kinematics
Chapter 5 Velocity Kinematics and Statics
Chapter 6 Inverse Kinematics
Chapter 7 Kinematics of Closed Chains
Chapter 8 Dynamics of Open Chains
Chapter 9 Trajectory Generation
Chapter 10 Motion Planning
Chapter 11 Robot Control
Chapter 12 Grasping and Manipulation
Chapter 13 Wheeled Mobile Robots

## Slide 2
Important concepts, symbols, and equations
We often define a fixed space frame {s} and a body frame {b} attached to some body of interest. All frames are instantaneously stationary.
Right-handed frames, and right-hand rule for positive rotation.
Special orthogonal group SO(3): matrices R in ℝ3×3 where RTR = I, det R = 1. R is a rotation matrix. Implicit representation with 9 numbers for 3 dof.
orthogonal
special

## Slide 3
Important concepts, symbols, and equations (cont.)
A group is a set of elements G = {a, b, c ...} and a binary operation • satisfying
closure a • b ∈ G for all a, b ∈ G
associativity (a • b) • c = a • (b • c)
identity element exists there is an I ∈ G such that a • I = I • a = a
for each a ∈ G
inverse exists for each a ∈ G, there exists a−1 ∈ G such that
a • a−1 = a−1 • a = I
Integers under addition? Nonnegative integers under addition? Square real matrices under multiplication?
What is a Lie group?

## Slide 4
Important concepts, symbols, and equations (cont.)
SO(3) is a matrix (Lie) group (the group operation is matrix multiplication).
  closure: R1R2 ∈ SO(3)
  associative: (R1R2)R3 = R1(R2R3) (not commutative! R1R2 ≠ R2R1 generally)
  identity: identity matrix I
  inverse: matrix inverse
  RTR = I, so R−1 = RT.
  For x ∈ ℝ3, ∥x∥ = ∥Rx∥.

## Slide 5
Important concepts, symbols, and equations (cont.)
Uses of a rotation matrix:
  Represent an orientation. Rab represents orientation of {b} in {a}.
  Change the reference frame of a vector or frame.
    subscript cancellation:
  Rotate a vector or frame. R = Rcd = Rot(ŵ, 𝜃), axis ŵ expressed in {c}.
p’c = Rcd pc (no subscript cancellation)
Rab’ = RRab (after rotating about axis in {a})
Rab’’ = RabR (after rotating about axis in {b})

## Slide 6
Rab =
pb =

## Slide 7
Given R1 = Rab, R2 = Rbc, and R3 = Rad,
write Rdc in terms of R1, R2, and R3 (no inverses!).
Given pb, what is pd in terms of R1, R2, and R3 (no inverses)?

## Slide 8
R = Rba = Rot(ŵ, 𝜃): 𝜃 = p/2, axis ŵ =
Rbc’ = RRbc = Rbc’’ = RbcR =

## Slide 9
orientation representation # nums imp/exp? pros cons
Euler angles, roll-pitch-yaw
Unit quaternions
Rotation matrices