## Slide 1
Chapter 2 Configuration Space
Chapter 3 Rigid-Body Motions
3.2 Rotations and Angular Velocities
Chapter 4 Forward Kinematics
Chapter 5 Velocity Kinematics and Statics
Chapter 6 Inverse Kinematics
Chapter 7 Kinematics of Closed Chains
Chapter 8 Dynamics of Open Chains
Chapter 9 Trajectory Generation
Chapter 10 Motion Planning
Chapter 11 Robot Control
Chapter 12 Grasping and Manipulation
Chapter 13 Wheeled Mobile Robots

## Slide 2
Important concepts, symbols, and equations
SO(3) is a curved 3-dimensional space, but the feasible velocities at any point of SO(3) form a flat 3-dimensional vector space (the “tangent space”).
Any rotational velocity can be expressed as an
angular velocity 𝜔 ∈ ℝ3, which can be considered
the product of a unit axis (in S2) and a speed
(a scalar).
Special orthogonal group SO(3): matrices R in ℝ3×3 where RTR = I, det R = 1. R is a rotation matrix. Implicit representation with 9 numbers for 3 dof.
Another example: the tangent space at a point of S2.

## Slide 3
Important concepts, symbols, and equations (cont.)
Given p ∈ ℝ3 and 𝜔 defined in the same reference frame, ṗ = 𝜔 × p.
Linear algebra notation: ṗ = 𝜔 × p = [𝜔] p, where
∈ so(3), the 3×3 real skew-symmetric
matrices (satisfying [x] = −[x]T).
so(3) describes the possible Ṙ when R = I, and
it is called the Lie algebra of the Lie group SO(3).

## Slide 4
Important concepts, symbols, and equations (cont.)
If Rsb = [p1 p2 p3], then Ṙsb = [ [𝜔s] p1 [𝜔s] p2 [𝜔s] p3 ] = [𝜔] Rsb.
Expressing the angular velocity in a different frame:
𝜔b = Rbs 𝜔s = R-1sb 𝜔s = RTsb 𝜔s 𝜔s = Rsb 𝜔b
The so(3) representations:
  [𝜔b] = R-1sb Ṙ = RTsb Ṙ [𝜔s] = Ṙ R-1sb = Ṙ RTsb
Exponential coordinate (axis-angle) representation of orientation: 𝜔𝜃
^

## Slide 5
Important concepts, symbols, and equations (cont.)
Scalar first-order linear diffeq:
Vector first-order linear diffeq:
matrix exponential

## Slide 6
Important concepts, symbols, and equations (cont.)
Integrating an angular velocity
Matrix exponential and matrix log:
Rodrigues’ formula