## Slide 1
Chapter 2 Configuration Space
Chapter 3 Rigid-Body Motions
3.2 Rotations and Angular Velocities
3.3 Rigid-Body Motions and Twists
Chapter 4 Forward Kinematics
Chapter 5 Velocity Kinematics and Statics
Chapter 6 Inverse Kinematics
Chapter 7 Kinematics of Closed Chains
Chapter 8 Dynamics of Open Chains
Chapter 9 Trajectory Generation
Chapter 10 Motion Planning
Chapter 11 Robot Control
Chapter 12 Grasping and Manipulation
Chapter 13 Wheeled Mobile Robots

## Slide 2
Important concepts, symbols, and equations
The special Euclidean group SE(3) is a matrix Lie group also known as the group of rigid-body motions or homogeneous transformation matrices in ℝ3 .
The inverse of T ∈ SE(3) is

## Slide 3
Important concepts, symbols, and equations (cont.)
Three uses of HT matrices:
  Represent a configuration. Tab represents frame {b} relative to {a}.
  Change the reference frame of a vector or frame.
  Displace a vector or frame. T = (R, p) = Trans(p) Rot(,𝜃)
v should be written in
homogeneous coordinates,
v = [v1 v2 v3 1]T.

## Slide 4
Important concepts, symbols, and equations (cont.)
Space-frame transformation:
Tsb’’ = T Tsb = Trans(p) Rot(,𝜃) Tsb
Body-frame transformation:
Tsb’’ = Tsb T = Tsb Trans(p) Rot(,𝜃)
1. rotate {b} by 𝜃 about
in{s} to get {b’}
(moves {b} origin)
2. translate {b’} by p
in {s} to get {b’’}
1. translate {b} by p
in {b} to get {b’}
2. rotate {b’} by 𝜃 about
in{b’} to get {b’’}

## Slide 5
Important concepts, symbols, and equations (cont.)
Any rigid-body velocity can represented as a screw axis (a direction ∈ S2, a point q ∈ ℝ3 on the screw, and the pitch (linear speed/angular speed) of the screw h), plus the speed along the screw .
q
If h is infinite, is the linear speed.
Otherwise, it is the angular speed.

## Slide 6
Important concepts, symbols, and equations (cont.)
The twist Va = (𝜔a , va) ∈ ℝ6 is the angular velocity expressed in {a} and the linear velocity of the origin of {a} expressed in {a}.
q
spatial twist Vs
body twist Vb

## Slide 7
Important concepts, symbols, and equations (cont.)
To transform a twist from one frame to another,
Va = Tab Vb
Va = [AdTab] Vb , where the adjoint representation of T = (R , p) is
4×4
6×1

## Slide 8
Important concepts, symbols, and equations (cont.)
Matrix representation of twists:
where se(3) is the Lie algebra of SE(3) (the set of all possible when T = I).

## Slide 9
Important concepts, symbols, and equations (cont.)
Screws and twists:
•
•
•

## Slide 10
Screws and twists
•
•
•
q
What is the dimension
of the space of screws?

## Slide 11
For J4, what is the screw axis Sb? Ss?
For J2?
Kinova lightweight 4-dof arm

## Slide 12
pb = (3,3,0)
Write Tbc.

## Slide 13
A camera with frame {c} tracks the optical marker on a tool to get its frame {t} relative to {c}. This transformation is T1. A space frame {s} is attached to the floor of the room, and the camera observes its configuration relative to {c} as T2. A robot arm has a mounting frame {m} which has been measured relative to {s} as T3. The arm’s encoders and the robot’s kinematics tell us the gripper’s frame {e} relative to {m}. This is represented as T4. The gripper should be at the frame {g} relative to {t} to be able to close on the tool and pick it up. This configuration is represented as T5.
Write Teg, the configuration of the grasping frame {g} relative to the current end-effector frame {e}, in terms of T1, T2, T3, T4, and T5.